## Slide 1: A monitoring method for after-earthquake damage evaluation of buildings final exam – 22 April 2015
Candidate:
Davide Trapani
Tutor:
Professor Daniele Zonta

## Slide 2: MOTIVATION
Following major earthquake it is critical identifying as soon as possible which buildings are safe for using and which are not in case of aftershocks;
Damage evaluation is done by on site visual inspections
Visual-based surveys are time-consuming and often subjective;
Emilia earthquake (DPC, 2013) | 
Surveys | 39000
Usable / Damaged | 36% / 64% (14000 / 25000)
Economic loss | 12.4 billion euro
Economic loss for industry | 5.4 billion euro (3,1 billion due to a halt in production)
Notes: Following a seismic event, a rapid damage evaluation is critical in order to identify as soon as possible which buildings are safe and which are not in case of possibile aftershocks. Currently damage evaluation is carried out mainly by on-site visual inspections, which are time-consuming, often subjective and sometimes uncertain. The evaluation of damage has to be performed as fast as possible in order to enable people to return home and social and economical activities to restart, limiting thereby the indirect costs associated with the earthquake.
As an example, I reported in this table some information related to the earthquake in Emilia. What I want to stress are in particular the total of 14000 inspections having as result the immediate usability and the total cost of 3.1 billion euro due to a halt in industrial production.

## Slide 3: RAPID EVALUATION BY MONITORING
Monitoring systems can limit the time required for damage evaluation:
    provide immediate information about usability;
    provide objective data on structural response for detailed evaluation;
To do this they must be reliable;
To be reliable they must be rationally designed basing on a logical path
Notes: Recently, monitoring systems supporting damage evaluation are gaining more and more attention by researchers and companies. A network of seismic monitoring systems can limit the time required for damage evaluation, providing immediate information on usability of building based on objective data on structural response.
To do this monitoring systems must be reliable and therefore rationally designed and based on a logical path.

## Slide 4: OBJECTIVES
Provide a framework for the design of seismic monitoring systems and the evaluation of their performance;
Evaluate the performance of monitoring systems based on Interstory Drift Ratio;
Develop a new product for seismic monitoring of RC buildings expanding range of applicability of the common approach

## Slide 5
Principles of design of seismic monitoring systems
Interstory drift monitoring: theory
Interstory drift monitoring: application on case studies
    Memscon Project: seismic monitoring of RC buildings
    Area Project: seismic monitoring of precast industrial buildings
I-Kubed Project: interstory drift monitoring from acceleration and tilt measurements
Conclusions
OUTLINE
Notes: The first topic of my presentation relates therefore to the principles of design of seismic monitoring systems. Then I will discuss how we can apply these principles in the design of systems based on interstory drift monitoring through three case studies relating to reinforced concrete buildings and precast industrial buildings.
Relates to, refers to, is in relation in to

## Slide 6: SEISMIC SHM
Aim: Infer the state of condition of the structure
By means of:
    definition of a state variable representing the state of condition
    collection of observations Y;
    model relating observation to state parameter
LOGIC
STATE
VARIABLE
Notes: From the logical point of view, the seismic monitoring problem means to infer the state of the structure after an earthquake. This can be done by defining a metric for the quantification of the state, this is the state parameter, the collection of a set observations UAI of the structural response, and the definition of a model relating state paramater to observations.

## Slide 7: SEISMIC SHM
TECHNOLOGY
Notes: From the technological point of view, a seismic monitoring system consists of a network of sensors placed inside the building, trasforming mechanical quantitities in electrical quantities and a data acquisition unit performing conversion to digital quantities. The storage of data in a database can be local or remote.

## Slide 8: System design vs structural design
 | Structural design | Monitoring system design
Need | Ensure stability of structural components | Infer the state of condition of the structure
Demand | Seismic loads | Required accuracy of the state variable
Model | Relation between loads and stress | Relation between observations and state variable
Capacity | Seismic capacity of structural components | Expected accuracy of the state variable
Check | Seismic capacity higher than seismic load | Expected accuracy higher than requested accuracy
Notes: The design of such a system presents some analogies with tradition structural design.
In structural design our need is to ènsure structural stability given the design demand, for example in terms of seismic loads. We design the structure and we verify by means of a model that the capacity of the structure in terms of seismic loads is higher than the demand.
In monitoring system design our need is to infer the state of condition of the structure with a certain level of accuracy, which is the design dimànd. We design the monitoring system and we verify by means of a model relating observations to state variable that the capacity expressed in terms of excected accuracy is higher than the demand.

## Slide 9: capacity-demand design approach
Need definition
State variable choice
Accuracy demand definition
Monitoring strategy definition
Accuracy capacity calculation
Capacity > Demand ?
YES
NO
FINAL DESIGN
Design drawings
Software
Installation
Maintenance Plan
Notes: The logical path we can use in the design of a monitoring system consists therefore of the following steps: definition of the needs of monitoring, choice of the state variable, definition of the accuracy demand and of the monitoring strategy, and calculation of the expected accuracy capacity. At this point if the accuracy capacity is higher than demand it is possibile to define the final design of the system, while if it is lower, it is necessary to reconsider the monitoring strategy.

## Slide 10: EXAMPLE
EXAMPLE
need: know the residual displacement d between 2 floors
Notes: In the following I will explain the various steps of the process with the help of an example. Let assume for instance that we want to know the relative displacement delta between the two consecutive floors of THIS FRAME.

## Slide 11: CHOICE OF THE STATE VARIABLE
state variable = logical or numerical variable representing state of condition
most used for seismic monitoring:
Type | Examples
Response parameters | Max accelerations; Max displacements; Residual displacements;
Modal parameters | Frequencies; Mode shapes; Damping;
Index of classification | classification of damage: no / moderate / severe / collapse Others
Notes: The first step is the ciois of the state variable which is the logical or numerical variable representing the state of condition of the monitored structure. The most widely used state variables used in seismic monitoring are response paramaters, such as maximum accelerations and maximum displacements and modal parameters, such as frequencies, mode shapes and damping ratios. Another possibility is assuming an index of classification, such as the standard classification reported in codes (no damage, moderate damage, severe damage and collapse) or others indices such as the Park & Ang index.

## Slide 12: CHOICE OF THE STATE VARIABLE
State variable choice
relative residual displacement d
Type | Examples
Response parameters | Max accelerations; Max displacements; Residual displacements;
Modal parameters | Frequencies; Mode shapes; Damping;
Index of classification | classification of damage: no / moderate / severe / collapse Others
state variable = logical or numerical variable representing state of condition
most used for seismic monitoring:
Notes: In our example we have to say if there is a lean in the frame at the end of motion and we can choose as state variable the relative residual displacement delta between the floors

## Slide 13: ACCURACY DEMAND DEFINITION
Type of state variable | Accuracy definition
Response parameters Modal parameters | Maximum error of the estimate; Standard deviation; COV;
Index of classification | Probability of state misclassification;
accuracy demand = design input parameter
State variable choice
relative residual displacement d
Accuracy demand
Notes: At this point we have to define the accuracy demand. The way we define the accuracy depend on the nature of the state variable, and in particular if the state variable is a number we can express the accuracy in terms of maximum error, standard deviation, coefficient of variation. If the state variable is an index of classification, the accuracy can be expressed in terms of probability of misclassification.

## Slide 14: ACCURACY DEMAND DEFINITION
accuracy demand = design input parameter
State variable choice
relative residual displacement d
Accuracy demand
uncertainty sd = 1 mm
Type of state variable | Accuracy definition
Response parameters Modal parameters | Maximum error of the estimate; Standard deviation; COV;
Index of classification | Probability of state misclassification;
Notes: In our example we have a state variable which is a response paramater, so we define the accuracy in terms of standard deviation of the estimation of delta.

## Slide 15: DEFINITION OF THE MONITORING STRATEGY
Definition of:
physical quantity to be observed;
measurement range;
number and location of sensors;
State variable | Physical quantities
Modal parameters | Acceleration while in service; Temperature;
Response parameters | Acceleration Displacement
State variable choice
relative residual displacement d
Accuracy demand
Observation
Range
uncertainty sd = 1 mm
Notes: Now we have to define the monitoring strategy. The definition of the monitoring strategy includes the definition of the physical quantity to be observed, the definition of the measurement range and the definition and number of observations.

## Slide 16: DEFINITION OF THE MONITORING STRATEGY
State variable choice
relative residual displacement d
Accuracy demand
Observation
Range
inclination Y
± 30 mrad
uncertainty sd = 1 mm
Y
Notes: In our example we decide to observe the inclination PSI of a shaft linking the floors in the range plus minus tirty milliradian

## Slide 17: DEFINITION OF THE model
model = logical relation between observations y and state variable θ
it includes:
      assumptions;
      signal processing techniques;
      numerical algorithms;
types of model:
      kinematic models;
      physical & mechanical models;
      heuristic models
State variable choice
Accuracy demand
Observation
Range
inclination Y
± 30 mrad
Model
relative residual displacement d
inclination Y
uncertainty sd = 1 mm
Notes: The last aspect to be defined is the model. The model is the logical relation between the observations UAI and the state variable FITA. In the definition of the model we have to include assumptions, signal processing techniques and numerical algorithms. Possible types of models are kinematic models, physical and mechanical models and heuristic models.

## Slide 18: DEFINITION OF THE model
State variable choice
Accuracy demand
Observation
Range
inclination Y
± 30 mrad
Model
relative residual displacement d
inclination Y
uncertainty sd = 1 mm
Y
Notes: In our example we use a simple kinematic model and in particular we define the state variable delta as the product of the observations PSAI by the interstory height EICH.

## Slide 19: Expected capacity
Expected instrumental and model uncertainties (max errors or standard deviation )
In terms of maximum error:
In terms of standard deviation:
Capacity
State variable choice
Accuracy demand
Observation
Range
± 30 mrad
Model
relative residual displacement d
inclination Y
uncertainty sd = 1 mm
Notes: At this point we are ready for calculating the expected capacity. We have to calculate all the uncertainties, instrumental and of the model, and combine them deterministically, calculating in this case the maximum possible error of the estimate, or probabilistically, in terms of standard deviation of the estimate.

## Slide 20: Expected capacity
Capacity
State variable choice
Accuracy demand
Observation
Range
± 30 mrad
Model
relative residual displacement d
inclination Y
uncertainty sd = 1 mm
Expected instrumental and model uncertainties (max errors or standard deviation )
In terms of maximum error:
In terms of standard deviation:
Notes: In the example the uncertainties are the uncertainty in the measurement of the angle, sigmapsai, and in the measurement of the heigth, sigmaeich. We combine them using the error propagation rule and as result, we obtain the accuracy on the state variable delta, to be compared to the demand

## Slide 21: SUMMARY 1
We monitor to infer the state of the structure after the earthquake;
A monitoring system is effective if it provides accurately the state variable
We can use a capacity-demand design approach in terms of state variable accuracy;
Calculation of capacity requires calculation of instrumental and model uncertainties;
Notes: To summarize this part,
We use monitoring to infer the state of condition of the monitored structure and we quantify the state by means of a state variable.
When we design a monitoring system we can follow a capacity demand approach in terms of the accuracy of the state variable.
The calculation of the capacity requires the estimation of all uncertianties involved in the monitoring process. The designed system is effective if it provides the state variable with adequate accuracy.

## Slide 22
Principles of design of seismic monitoring systems
Interstory drift monitoring: theory
Interstory drift monitoring: application on case studies
    Memscon Project: seismic monitoring of RC buildings
    Area Project: seismic monitoring of precast industrial buildings
I-Kubed Project: interstory drift monitoring from acceleration and tilt measurements
Conclusions
Notes: Having discussed the design principles, now can apply them to the problem of interstory drift monitoring.
Relates to, refers to, is in relation in to

## Slide 23
DAMAGE IN RC BUILDINGS
Interior partition walls
Exterior walls
Shear failure of columns
Soft storey collapse
Buckling of rebars
Notes: however, first I would recall the possible damage that can occur in reinforced concrete buildings. Damage can occur in non structural elements, for example in exterior walls or in partition walls, or in structural elements, in particular in columns.

## Slide 24
INTERSTORY DRIFT RATIO AS STATE VARIABLE
It is the ratio of the relative horizontal displacement between 2 consecutive floors to the storey height
It can be related to non-structural damage:
It can be related to structural damage:
More detailed limit definition is possible, for example in the context of a vulnerability assessment
Drift limit | Serviceability | Damage Control
brittle elements | 0.004 | 0.025
ductile elements | 0.007 | 0.025
detailed elements | 0.010 | 0.025
(Sullivan et al. 2012):
Performance Level | Peak | Residual
Fully operational | 0.002 | ≈ 0
Operational | 0.005 | ≈ 0
Life-safety | 0.015 | 0.005
Near Collapse | 0.025 | 0.025
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
(Priestley et al. 2007):
Notes: The interstory drift ratio is defined as the ratio of the relative horizontal displacement between two consecutive floors and the storey height. If we know the interstory drift ratio experienced by the building during the earthquake, we can estimate the level of damage by comparing it to code limits, or better, to limits obtained from a non linear analysis of the building, for example in the context of a vulnerability assessment.

## Slide 25: OBSERVATIONS
Observations: accelerations - range +- 2 g;
Number and location: at least 3 measurements along 2 horizontal directions at each floor of the building or at relevant floors;
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
FLOOR 0
FLOOR 1
FLOOR 2
FLOOR j
Notes: Assuming interstory drift ratio as state variable, the most common monitoring strategy consists of the observations of horinzontal accelerations at each level of the building using accelerometers…

## Slide 26: MODEL
Nature of the model: algorithmic
1) Processing of acceleration signals: baseline correction; high-pass filtering;
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
ACCELERATION MEASUREMENTS
SIGNAL PROCESSING
DISPLACEMENT
(DOUBLE INTEGRATION)
STOREY DISPLACEMENT
IDR CALCULATION
IDR CALCULATION
IDR
2) Displacement time histories:
3) Storey displacement
4) Interstory drift ratio
Notes: …and of the estimation of the intestory drift by means of an algorithmic model, relating observed accelerations to interstory drift.
In particular the model consists of the processing of acceleration signals, the calculation of displacement time histories from numerical double integration, the calculation of story displacements and rotation and in the calculation of interstory drift.
Given this model, what we have to do now is calculate the uncertainy in the estimation of the interstory drift. We have two types of uncertainties, instrumental uncertainties and model uncertainties.

## Slide 27: instrumental uncertaintY (1/2)
Type of error | MEMSIC CXL02TG3 | PCB 3711
Sensitivity(eS) | 0.03 | 0.01
Environmental (eE) | Not reported | 0.03
Misalignment (ea) | 0.01 | 0.00
Cross-axis sensitivity (ec) | 0.03 | 0.03
Installation (ei) | 0.02 | 
Errors affecting accelerometers (expressed as max errors in data sheets)
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Assuming a triangular distribution:
Combination:
can be compensated
Instrumental Uncertainty | MEMSIC CXL02TG3 | PCB 3711
Standard deviation | 0.056 | 0.048
We assume
in the following
Notes: Instrumental uncertainties are the uncertainties in the measurement of acceleration, and therefore depend on the sensor. In this table I reported the most important sources of uncertainty for two models of accelerometer, one produced by MEMSIC and the other by PCB Piezotronics. These value are typically reported in data sheets in terms of maximum value, so to obtain their standard deviation we can consider a triangular distribution. In order to obtain the overall uncertainty on the measurement we can use the rule of uncertainty propagation and find the value. We assume in the following an instrumental uncertainty equal to zero point zero six as an example, but I remark that this value must be determined on a case by case basis.

## Slide 28: INSTRUMENTAL UNCERTAINTY (2/2)
Noise in accelerometers: white noise + 1/f noise;
Noise effect amplified through the model (low frequency components);
It is necessary to apply an high-pass filter to acceleration signals;
Example (high noise instrument, MEMSIC CXL02TG3):
fcut [Hz] | Std [mm]
0.05 | 5.5
0.06 | 3.5
0.08 | 1.4
0.15 | 0.33
0.20 | 0.14
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Notes: The other source of instrumental uncertainty is noise. Noise in accelerometers can be modeled by the sum of white noise and pink noise. The effect of noise is amplified through the model when we calculate displacements from numerical integration, in particular at low frequencies. For this reason, it is always necessary to apply an high-pass filter to the acceleration signals.
In this graph I show as an example the result of the integration of noise only for different values of the cutoff frequency of the high-pass filter, while in the table I reported the standard deviation.

## Slide 29: MODEL UNCERTAINTIES - METHOD
Numerical evaluation of model uncertainty
1) generated acceleration and displacement time histories
2) Added white + pink noise to acceleration time histories;
3) Calculated displacement time histories from double integration
4) Calculated relative error:
Newmark’s
method
from ITACA database
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Notes: At this point it is necessary to determine the uncertainty due to the model, and in particular the error we make in terms of displacements when we integrate noisy acceleration signals.
To do this, I performed a numerical analysis on single degree of freedom systems applying different levels of ground excitations. In particular I generated a set of acceleration and displacement time histories for different frequencies of the system, I added white noise plus pink noise in order to simulate monitoring data, i double integrated the accelerations using different cutoff frequencies and I calculated the relative error between the displacement resulting from Newmark integration method and the displacement resulting from double integration method.

## Slide 30: MODEL UNCERTAINTIES – OUTCOMES 1/2
  Optimal HP cut-off frequency:
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
  In this range and for linear systems:
  Standard deviation of relative error due to model: 0.07
DESTRA:
f = 0.3/8
fc = 1.2
DESTRA:
f = 0.3/8
fc = TUTTI
Notes: In these two graphs I show the error in function of the ratio of the cutoff frequency to the frequency of the system. The first result of the analysis is that the optimum range of the cutoff frequency is between fiftheen percent and sixty percent of the frequency of the system. Below this range, the effect of noise becomes predominant, while above this range we cut components of the response of the system.
The second result is that the standard deviation of the error is basically indipendent of the frequencies and its value can be assumed as zero point zero seven.

## Slide 31: MODEL UNCERTAINTIES – OUTCOMES 2/2
  residual displacement dr is lost;
  peak displacement is underestimated
  Sections
    40x40
    50x50
    60x60
    70x70
  H = 6 m
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
  error increases linearly with residual;
Notes: When we perform the same analysis on non linear systems, we obtain that the residual displacement at the end of the record is totally lost and the displacements obtained from double integration are understimated. In particular, it can be seen that the error increases with the value of residual displacement. The effect of residual can be taken into account as an increase on the value of standard deviation of error up to 0.20.

## Slide 32: CAPACITY EVALUATION
Propagation of uncertainty through IDR estimation.
Let assume:
  instrumental uncertainty: 0.06
  numerical uncertainty: 0.07
Calculation of story displacement:
Let assume:
Displacement i at floor j
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Storey displacement
Notes: Having estimated separately instrumental uncertainties and uncertainties of the model, we can combine them obtaining that uncertainty is 0.09 on the displacement of the sensor location. Propagating this uncertainty in the calculation of story displacement we obtain that uncertainty is 0.06 on the displacement of the floor.

## Slide 33: CAPACITY EVALUATION
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Calculation of interstory drift ratio
H = 3 m
IDR = 0.001 | 
D [mm] | s [-]
2.5 | 10%
5.5 | 20%
16 | 50%
IDR = 0.005 | 
D [mm] | s [-]
9.0 | 10%
27.0 | 20%
63.0 | 50%
Notes: Propagating again the uncertainty in the calculation of the interstory drift ratio, we obtain that it depends on the values of the displacements of the floors. In particular it is possible to obtain, using the formula or a graph like this, the value of the uncertainty given the value of the displacement of the lower floor and the value of the interstory drift.
ten to the power of minus 3

## Slide 34: SUMMARY 2
A possible state variable for after-earthquake damage evaluation is interstory drift ratio (IDR);
The most common approach for obtaining IDR is based on numerical integration of acceleration observations.
From numerical analysis we have found that:
  the optimum range for cutoff frequency is
  high errors are introduced in case of residual displacements;
The uncertainty on IDR is proportional to displacement of the floors and inversely proportional to the story height
Notes: We can summarize this second part as follows:

## Slide 35
Principles of design of seismic monitoring systems
Interstory drift monitoring: theory
Interstory drift monitoring: application on case studies
    Memscon Project: seismic monitoring of RC buildings
    Area Project: seismic monitoring of precast industrial buildings
I-Kubed Project: interstory drift monitoring from acceleration and tilt measurements
Conclusions
Notes: Let move on to the analysis of the first case study, which refers to Memscon project.
Relates to, refers to, is in relation in to

## Slide 36
11 partners from 7 countries
Universities
Companies
Consultants
MEMSCON PROJECT
Notes: Memscon Project was an European Project started in 2008 and concluded in 2012…

## Slide 37
AIM
Development of a reliable and cost-effective monitoring system to be integrated in new RC buildings for their protection against earthquake and settlement.
OBJECTIVES
(i) development of a wireless MEMS sensor network, including creation of new dedicated instruments for strain and acceleration measurement.
(ii) development of a Decision Support System (DSS) for remote data processing, structure condition assessment and for maintenance planning.
MEMSCON PROJECT
Notes: …which aimed at the development of a reliable and cost-effective monitoring system for reinforced concrete buildings fort their protection against earthquake and settlements.
In particular, the main objectives of the project were the development of a wireless MEMS sensor network for the measurement of strain and acceleration, and the development of a Decision Support System for structural condition assessment and maintenance planning.

## Slide 38: System architecture
The system includes a wireless network within the building and a base station linking the building to a remote data interpreter.
Strain measurements are collected at the lowest level of the building, to estimate the vertical column loads and any variation due to settlement;
Horizontal acceleration is measured by dedicated nodes at each level during an earthquake, allowing analysis of the seismic response of the whole structure.
Notes: The system includes a wireless network of acceleration and strain sensors, a base station and a remote data interpreter.
Strain sensors are placed at the interface between columns and foundations, in order to estimate vertical load in columns.
Accelerometers are instead placed at each floor of the building so in the same locations as in the previous part of the discussion.

## Slide 39: MEMSCON WIRELESS ACCELEROMETER
X
Y
Z
SPECIFICATIONS
Tri-axial MEMS capacitive accelerometer
Sampling rate: 200Hz
Resolution: 16bit
Range: from -2g to +2g (from -20m/s2 to +20m/s2)
Sensitivity: 170-300 mV/g
Notes: Here are some specifications of the Memscon wireless accelerometer. The Memscon Accelerometer is a triaxial MEMS capacitive accelerometer specifically designed for the application. Its main features are 2 hundreds sampling rate, sixtiin bit resolution, range between minus 2g and plus 2g and sensitivity between 1 hundred and seventy and 3 hundreds millivolt over g.
In the packaging we can identify the MEMS sensor, the microprocessor, the memory, the lithium battery and the antenna.

## Slide 40: MEMSCON MONITORING STRATEGY
ACCELERATION MEASUREMENTS
SIGNAL PROCESSING
DISPLACEMENT
(DOUBLE INTEGRATION)
STOREY DISPLACEMENT
IDR CALCULATION
IDR CALCULATION
IDR
1) State variable = Interstory Drift Ratio
2) State variable = Park & Ang Index (Park, Y J, and A H S Ang. 1985)
ACCELERATION MEASUREMENTS
SIGNAL PROCESSING
DISPLACEMENT
(DOUBLE INTEGRATION)
STOREY DISPLACEMENT
POST-EVENT REMOTE NON LINEAR ANALYSIS
IDR CALCULATION
D
Notes: Using Memscon system we can choose two possible state variables for after-earthquake damage evaluation.
The first is Interstory Drift Ratio and in this case the model linking the observation of accelerations and the state variable is always the same.
The second is the Park & Ang damage index, which takes into account not only the maximum ductility demand, but also the contribution of energy dissipation. In this case the model is the same up to the calculation of storey displacement, then a non linear dynamic analysis of the building is performed calculating finally the index.
In this presentation I will discuss the first method…

## Slide 41: TEST on full-scale 3d frame
AIM:
To assess the reliability of the whole Memscon system performing different tests on a 3D concrete frame
TEST EXECUTION
EQ-like displacement time histories at the top
Different amplitudes
Different levels of damage
Notes: …And in particular the evaluation of the system on a full-scale threedimensional frame tested dynamically in laboratory conditions. The tests in particular consisted in the application at the top of frame of earthquake-like displacement time histories with increasing amplitude, in order to induce different levels of damage.

## Slide 42: SPECIFICATIONS OF THE FRAME
Notes: Here are some specifications of the frame. The dimensions of the frame were 3 by 3 meters in plane and 3.20 meters in elevation.
The dimensions of the column cross sections are thirty by thirty centimeters, while the dimensions of the beams are thirty by fifty centimeters. The thickness of the concrete slab at the top of the frame was twelve centimeters

## Slide 43: DYNAMIC TEST - SETUP
Vertical actuator
Horizontal
actuator
1 Steel beam connected to the vertical actuator
2 Steel beams supporting the beam above and supported by the r.c. columns
Vertical load is applied from below. The actuator is anchored to a steel beam above the slab. It is supported by 2 steel beams directly connected to the frame columns.
Horizontal load is applied directly to the rigid slab.
Notes: Here are instead some details about test setup. In particular we have an horinzontal actuator for the dynamic application of displacements, and a vertical actuator for the application of the vertical load. We also have a mechanical system of steel beams which is used for the transfer of the forces.

## Slide 44: DYNAMIC TEST INSTRUMENTATION
Notes: Here are instead the position of the accelerometers, in particular I placed two Memscon accelerometers close to comumn 3 and other 2 close to column 2. I placed in the same positions also seismic accelerometers as reference.

## Slide 45: DYNAMIC TEST – SEQUENCE OF TESTS
Also a static test performed after each dynamic test
Notes: The horizontal actuator was set in order to produce the seismic response of a single degree of freedom system with natural frequency 1.5 Hz. The load protocol consists therefore in the application of the vertical load up to 600 kN, on the application of the horizontal displacement and on the unloading.
I defined the sequence of tests assuming as reference the expected displacement at yielding, 17 millimetres, and scaling the maximum displacement from 25% to 500% of this value. Moreover, after each test a static test was also performed.

## Slide 46: TEST IN ACTION
D = 68 mm
PFA = 0.51 g
Notes: Here is a video on one of the test, in particular the test producing a maximum displacement of sixtyeight millimeters and a peak floor acceleration of 0.5 g

## Slide 47: OUTCOMES - OBSERVED DAMAGE
Cracking at the bottom of columns
Horizontal cracks
(stirrups)
Cracking
diffusion
Yielding
Spalling at the bottom
 | Park & Ang Damage Index |  |  |  | 
 | 3D frame | C1 | C2 | C3 | C4
crack | 0.199 | 0.199 | 0.138 | 0.122 | 0.156
100% Dy | 0.264 | 0.219 | 0.223 | 0.243 | 0.264
200% Dy | 0.397 | 0.316 | 0.325 | 0.397 | 0.382
300% Dy | 0.467 | 0.467 | 0.452 | 0.402 | 0.414
Park & Ang
damage states:
D = 4 mm
D = 13 mm
D = 17 mm
D = 51 mm
D = 85 mm
Notes: Here are the observed levels of damage after each test. After test at 25% the yielding displacements, the cracking at the bottom of the columns was observed. Then, it was observed the diffusion of cracking up to yielding of the reinforcement, occurred for a displacement of 51 mm hence three times the expected displacement, as it can be observed from the force-displacement curves. The damage index has been calculated using the software provided within the Project. It can be seen that the result is reliable, with a value of the index about 0.5 which represent a moderate severe damage.

## Slide 48: OUTCOMES - DISPLACEMENTS
Test | MTS | M102 | M103 | M104 | M106
25% Dy | 5.50 | 5.6 | 5.4 | 5.4 | 5.6
100% Dy | 21.56 | 21.5 | 21.4 | 21.5 | 19.7
300% Dy | 52.31 | 49.7 | 47.0 | 46.9 | 34.4
Test | MTS | M102 | M103 | M104 | M106
25% Dy | 5.50 | -0.018 | 0.018 | 0.018 | -0.018
100% Dy | 21.56 | 0.003 | 0.007 | 0.003 | 0.086
300% Dy | 52.31 | 0.050 | 0.102 | 0.103 | 0.342
Dmax
Error
Notes: At this point we can obtain an estimation of the uncertainty in terms of displacements by comparing the displacements obtained from Memscon system to the displacement actually applied to the frame.

## Slide 49: MEMSCON IDR MONITORING - evaluation
From experimental tests (perfectly calibrated sensors, relative to this earthquake):
Error on max displacement of the floor:
    std error: 0.044
Comparison between performance levels, IDR values and observed damage
Storey displacement
Interstory drift ratio
Test | REAL | M102 | M103 | M104 | M106
25% Dy | 0.0020 | 0.0021 | 0.0020 | 0.0020 | 0.0021
100% Dy | 0.0080 | 0.0080 | 0.0079 | 0.0080 | 0.0073
300% Dy | 0.0194 | 0.0184 | 0.0174 | 0.0174 | 0.0127
Performance Level | Peak
Fully operational | 0.002
Operational | 0.005
Life-safety | 0.015
Near Collapse | 0.025
Actual Yielding
IDR VALUES
Cracking
Notes: Using perfectly calibrated sensors, and for this particular earthquake, I obtained an uncertainty in the estimation of the storey displacement of 0.044 which, propagating it through the calculation of IDR leads to a value of uncertainty in IDR in line with the results of numerical analysis.
We can also compare the observed damage, the measured interstory drift and the limits relative to different performance levels.
For a IDR of 2 per mil, which corresponds to the fully operational performance level, we observed small cracks in columns, while for an IDR of 2%, which exceeds the life safety performance level, we observed the actual yielding of the columns.

## Slide 50
Principles of design of seismic monitoring systems
Interstory drift monitoring: theory
Interstory drift monitoring: application on case studies
    Memscon Project: seismic monitoring of RC buildings
    Area Project: seismic monitoring of precast industrial buildings
I-Kubed Project: interstory drift monitoring from acceleration and tilt measurements
Conclusions
Notes: On this point we can move to the second case study which refers to the seismic monitoring of precast industrial buildings.

## Slide 51: MONITORING OF PRECAST INDUSTRIAL BUILDINGS
Goal: development of a seismic monitoring system based on IDR for precast industrial buildings;
BRITTLE
Scope of application: new or retrofitted buildings compliant to seismic codes
BRITTLE
DUCTILE
Notes: Following the earthquake in Emilia region Area Prefabbricati, a company working in the field of precast building production contacted us asking for the development of a seismic monitoring system.
As reported in the literature, the surveys conducted in field after the earthquake highlighted that most of the damage in precast buildings were due to insufficient detailing between columns and beams, to the collapse of external walls and to the development of plastic hinges at the bottom of the columns.
In principle this last failure mechanism is the only one possible for well designed buildings, and can be monitored by means of a monitoring system based on IDR.
The scope of application of the monitoring systems which I developed for the company consists therefore in new or retrofitted buildings compliant to the seismic codes.

## Slide 52
PRECAST INDUSTRIAL BUILDINGS
Typical configuration:
Isolated foundations;
Cantilever columns;
Simply supported beams;
Simply supported roof elements;
2 bi-axial sensors per column
Displacements governed by roof modes of vibration
Notes: The typical configuration of a precast industrial building consists in cantilever columns supported by isolated foundations, beams simply supported by the columns and roof elements simply supported by the beams. This implies that we cannot place only two bi-axial accelerometers on the roof, because the assumption of DAIAFRAM behaviour is not valid, but rather we should place accelerometers at the top and at the bottom of each column. Being this impossible in practice, we need a logical methodology for determining the number of sensors to be arranged inside the building.

## Slide 53: DISPLACEMENT AT UNMEASURED LOCATION
measured node displacements
unmeasured node displacements
submatrix containing only rows
relative to measured nodes
submatrix containing only rows
relative to unmeasured nodes
node
displacement
vector
modal matrix
modal
coordinates
vector
Notes: This can be done by the modal decomposition of seismic motion, assuming that the node displacement vector EX R can be expressed as the product of the modal matrix FAI by the modal coordinate vector EITA. The node displacement vector can be subdivided into nodes displacements directly observed by a sensor EX M, and unknown nodes displacements EX U. At the same time, the modal matrix can be subdivided in a submatrix containing only rows relative to observed node displacements FAI EX M, and another containing only rows relative to not observed node displacements FAI EX U. After some algebra manipulation, it can be obtained that the unknown nodes displacement EX U can be expressed as the product of matrix M by the EX M, that is the unknown displacement can be obtained as a linear combination of the measured displacements.

## Slide 54: incompleteness of the field
Uncertainty on Xu depends on number of modes considered and on number and location of sensors;
Numerical analysis varying considered modes and sensors arrangement
on unmeasured nodes
(model M1)
M1
M2
M3
M4
Optimal number of sensors
2x(n+m)
Notes: In order to assess the effectiveness of this method I performed dynamic analysis on finite element models of precast buildings case studies. In particular, the problem here is to evaluate the uncertainties on the estimation of unknown displacements, in function of the number of modes considered in the modal matrix and of the number of placed sensors. I calculated this uncertainty for different arrangements by calculating it as the ratio of the displacements obtained from the application of the method to the displacement given by the finite element model.
I obtained that in order to limit uncertainties under 1% it is necessary to consider all the modes of vibration and to arrange a number of sensor equal to the number of modes. In other terms, it is necessary to arrange a sensor for each frame of the building on both directions.

## Slide 55: APPLICATION OF THE FRAMEWORK
State variable: IDR of each column;
Observations: acceleration
Number of sensors depending on the building
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Notes: So when we design a monitoring system for new precast industrial building we can assume IDR experienced by each column as state variable, we can observe acceleration at a number of locations which depends on the size of the building and in particular on the number of frames,…

## Slide 56: MONITORING STRATEGY
Nature of the model: algorithmic
1) Signal processing: baseline correction; band-pass filtering;
ACCELERATION MEASUREMENTS
DISPLACEMENTS
AT SENSOR LOCATION
DISPLACEMENTS AT OTHER LOCATIONS
IDR CALCULATION
IDR
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
2) Displacement time histories from double integration
SIGNAL PROCESSING
3) Displacement time histories from linear combination
4) Interstory drift ratio calculation
Notes: and we apply the usual model to obtain the state variable from the observations. The only one diffence is that the displacements of not instrumented columns are obtained from the linear combination of the displacements of the instrumented columns.

## Slide 57: System components
PCB 3711 Accelerometer
Master
DAQ Modules
PC
Slave
Notes: To design this system I used components available on the market. In particular I used high-end capacitive wired accelerometers model 3711 by PCB Piezotronics, a Master-Slave data acquisition architecture, needed in order to limit the length of the wires, and a desktop Pc for automatic data analysis.

## Slide 58: SOFTWARE
Notes: To develop the software I used Labview platform, here I reported some screens, if you are interested we can discuss about it at the end of the presentation.

## Slide 59: EXAMPLE
Notes: Here is instead an example of configuration of the system, we can see in particular the location of the accelerometers, of the master unit, of the slave unit and the cables.

## Slide 60: TYPE A EVALUATION of UNCERTAINTIES
Test Equipment:
Experimental tests:
  calibration of the whole measuring chain;
  comparison to laser transducer for different types of excitation;
Shaking table
Laser displacement transducer
Test setup
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Notes: Now we have to determine uncertainties.
In this case to test the performance of the system I used a shaking table producing different types of excitations, and laser displacement transducer as reference. In particular I carried out calibration tests of the whole measuring chain, that is sensors plus daq units plus software,

## Slide 61: OUTCOMES
Input | Max ΔM [mm] | Max ΔE [mm] | Err
L’Aquila 1 | 26.80 | 27.46 | -2.46%
L’Aquila 2 | 15.28 | 15.00 | 1.83%
Fivizzano | 12.80 | 13.30 | -3.91%
Mirandola | 16.70 | 14.90 | 10.78%
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
Test | Frequency [Hz] | Laser Peak [mm] | System Peak [mm] | Error
P1 | 0.5 | 10.82 | 11.07 | 2.26%
P2 | 0.5 | 22.04 | 22.34 | 1.34%
P3 | 1.0 | 5.46 | 5.58 | 2.15%
P4 | 1.0 | 11.15 | 11.31 | 1.41%
P5 | 1.0 | 22.74 | 22.50 | -1.07%
Notes: Here I reported some of the results, in particular I show the comparison between laser and monitoring system for sainusoidal time histories in the range of frequencies between 0.5 and 1.0 Hertz which is the range of interest for precast industrial buildings,
while here I show the same comparison in case of an earthquake shaking simulation.
Also in this case I calculated the uncertainty by comparing the response of the system to the reference…

## Slide 62: EVALUATION of the capacity
Displacements at sensors locations:
Instrumental error: 0.033
Model error: 0.047
State variable
Observation
Model
Instrumental Uncertainty
Model Uncertainty
Capacity
At sensors locations
Uncertainty of Interstory drift:
At others locations
H = 8m
Notes: obtaining that for the designed system the uncertainty on the displacement at measured locations can be assumed as equal to 0.06, while for the the displacements at unmeasured locations it basically depends on the number of measured displacements which are involved in the estimate.

## Slide 63: SUMMARY 3
Experience on case studies leads to the conclusion that:
  order of magnitude of uncertainty on IDR is confirmed
    using low cost accelerometer prototypes;
    using high-end accelerometers on the market;
The uncertainty of the estimate of IDR is governed by the model:
  amplification of noise at low frequencies;
  signal processing techniques;
  effect of the residual displacement;
Notes: The current approach for IDR estimation is based on a relative measurement of displacements obtained from accelerations. We have seen that the uncertainty of the estimate depends on signal processing, amplitude of the displacements and the value of the residual displacements.
So how can we reduce these uncertainties? We have to simplify the model relating state variable to observations, in particular directly measuring the interstory drift ratio.

## Slide 64
Principles of design of seismic monitoring systems
Interstory drift monitoring: theory
Interstory drift monitoring: application on case studies
    Memscon Project: seismic monitoring of RC buildings
    Area Project: seismic monitoring of precast industrial buildings
I-Kubed Project: interstory drift monitoring from acceleration and tilt measurements
Conclusions
Notes: The last part of my research deals with the study on a different model for IDR estimation.

## Slide 65
I-KUBED APPROACH
Goal: development of a monitoring system giving IDR as state variable basing on a kinematic model and able to:
  provide floor accelerations;
  provide real time IDR;
  provide residual IDR;
  Without the need of double integration and therefore of filtering
State variable
Observation
Model
Uncertainty evaluation
Prototype
Notes: In particular, the goal here is to develop a monitoring system of IDR based on a kinematic model able to provide real time floor accelerations, real time interstory drift and the possible residual value.

## Slide 66: PATENT PENDING sensing bar
hinged bar
joints
accelerometer stand;
accelerometer
Inclinometer
Protective case
State variable
Observation
Model
Uncertainty evaluation
Prototype
PENDING PATENT NUMBER: 102015000009772
Notes: This is possible using what I named the sensing bar, which is currently a patent pending product.
The sensing bar consists of a bar hinged to the floors instrumented with 2 bi-axial accelerometers measuring accelerations, one at each end of the beam, and one bi-axial inclinometer placed at the mid span of the bar measuring the tilt of the beam.

## Slide 67: OBSERVATIONS
Observations: 1) inclination – range +- 35 mrad
2) accelerations - range +- 2 g;
Number and location: 2 per floor (4 accelerations+ 2 inclinations)
bi-axial inclinometer
bi-axial accelerometer
State variable
Observation
Model
Uncertainty evaluation
Prototype
Notes: The observations we can make with this instrument are therefore inclinations and accelerations. We can place two sensing bars at each floor of the building as showed in this schema.

## Slide 68: HOW IT CAN BE USED
2)
Real time monitoring of IDR from acceleration and tilt measurements
IDR estimation from double numerical integration of accelerations
Residual IDR observation at the end of the motion from inclinometer
1)
Correction of Peak Interstory Drift based on Residual IDR value
Notes: The sensing bar can be used for the IDR calculation from double numerical integration of acceleration measurements, following the process I discussed previously, and for the IDR estimation at the end of the motion, providing therefore a further damage index. Moreover, the observed residual interstory drift can be used for the correction of the peak interstory drift, simply by adding the residual value to the peak value. As an example, I show in this graph the model error in the case the residual drift is unknows, in black crosses, and the model error in case the residual drift is known, in red crosses.
The other use of the sensing bar which I’m studying in this moment is the realtime monitoring of IDR obtained combining the measurements of acceleration and tilt

## Slide 69: MODEL
Nature of the model: kinematic
Compensation of accelerations applied to the inclinometer
INCLINATION MEASUREMENTS
COMPENSATION OF ACCELERATION
IDR
ACCELERATION MEASUREMENTS
State variable
Observation
Model
Uncertainty evaluation
Prototype
Notes: In this case we can use a kinematic model, consisting in the real time syncronos measurements of inclinations and accelerations, in the compensation of the accelerations and in the calculation of interstory drift.
The compensation of the acceleration is necessary because the inclinometer is sensitive not only to the acceleration of gravity but also to the acceleration applied. We have therefore defined a kinematic model which gives the tilt of the beam PSAI, hence the interstory drift ratio, given the angle measurement of the inclinometer alpha and the applied acceleration aPSAI obtained assumed a linear field of acceleration along the bar.

## Slide 70: LABORATORY TEST
Observed standard deviations: | 
0.5 Hz | 1.16 mm IDR 0.38 mrad
1.0 Hz | 1.08 mm IDR 0.36 mrad
State variable
Observation
Model
Uncertainty evaluation
Prototype
Test 0.5 Hz - +-25mm
Test 1.5 Hz - +-15mm
Notes: Here are the result of the preliminary tests I performed, carried out by fixing one end of the sensing beam to the shaking table and the other to the upper floor of the laboratory. Producing sinusoidal excitiation at frequencies 0.5 and 1.0 Hz I obtained a standard deviation in the maximum displacement about 1.0 mm, indipendent ot the amplitude.

## Slide 71: PROTOTYPE of the SYSTEM
2 Storeys
School building (Trentino)
Sensing bars: 2 per floor
Rack Sensing bar
Wires
State variable
Observation
Model
Uncertainty evaluation
Prototype
Notes: The system provided IDR from double integration of acceleration measurements and residual IDR at the end of the motion is currently installed inside a school building here in Trentino, here I report the position of the system components and the wires….

## Slide 72: INSTALLATION of the PROTOTYPE
State variable
Observation
Model
Uncertainty evaluation
Prototype

## Slide 73
PROTOTYPE OF THE SOFTWARE
State variable
Observation
Model
Uncertainty evaluation
Prototype
Notes: While here I show a screen of the software I developed for the application.

## Slide 74
SUMMARY 4
Developed a new product for monitoring which:
  provide also residual deformation as damage index;
  expand the applicability of double integration method to non linear field;
  allows for truly real time IDR monitoring with an accuracy of 0.3 mrad independent to the amplitude of motion;
This product is currently patent pending in Italy;
Prototypes of the system are being installed in Trentino by the start-up company I-Kubed I co-founded (www.i-kubed.com)

## Slide 75
Principles of design of seismic monitoring systems
Interstory drift monitoring: theory
Interstory drift monitoring: application on case studies
    Memscon Project: seismic monitoring of RC buildings
    Area Project: seismic monitoring of precast industrial buildings
I-Kubed Project: interstory drift monitoring from acceleration and tilt measurements
Conclusions

## Slide 76: Conclusions
Defined a capacity-demand approach in terms of accuracy of the information provided by the system which can be used for the design and performance evaluation of monitoring systems;
Investigated numerically and experimentally the performance of IDR estimation from observation of accelerations only ;
Developed a commercial seismic monitoring system for precast industrial buildings based on the current approach of IDR monitoring;
Developed a new monitoring product based on kinematic model for the direct measurement of IDR in real-time expanding the applicability to inelastic field.
Notes: In this research I…

## Slide 77: Future work
Implementation of probabilistic approach by means of fragility curves based on IDR estimation from monitoring;
Industrial development of the sensing bar:
    integration of sensors and ADC within sensing bar;
    wireless transmission capability;
Notes: Future work of this research are…

## Slide 78: ACkNOWLEDGEMENTS
This research was partially funded in the context of MEMSCON project (EC Seventh Framework Programme Grant Agreement n. CP-TP 212004-2) and by Area Prefabbricati S.p.A.
I wish to thank all people involved in the MEMSCON project and in particular project coordinators Manthos Bimpas and Angelos Amditis.
I wish also thank Emanuel Manfredini, Moreno Manfredini and Antonello Gasperi for their fundamental support.
I wish also to mention the Mayor of Stenico, Dott.sa Monica Mattevi, for the interest in SafeQuake, commercialized by IKubed S.r.l. and based on my research.
Notes: Before closing I wish to thank all people involved in Memscon Project and Area Project for their support.

## Slide 79: A monitoring method for after-earthquake damage evaluation of buildings final exam – 22 April 2015
Candidate:
Davide Trapani
Tutor:
Professor Daniele Zonta
Thanks for your attention
Notes: Thank for your attention!

## Slide 80
POSSIBLE MONITORING TECHNIQUES
Seismic Intensity Measures (IM)
Engineering Demand Parameters (EDP)
Structural Parameters
GA – Ground acceleration time history
PGA – Peak Ground Acceleration
PGV – Peak Ground Velocity
SPA – Response Spectral Pseudo-Acceleration
PFA – Peak Floor Acceleration
PID – Peak Interstory Drift Ratio
MSD – Maximum Shear Demand
SID – System Identification
MU – Modal Updating
Observation of ground excitation
Observation of structrural response
Comparison between pre and post event paramaters
Notes: To assess from monitoring these type of damage we can use different monitoring techniques. We can relate damage on a measure of seismic intensity, to an engineering demand parameter or to a variation of structural paramaters between before and after the seismic event.
In my research I focused mainly on monitoring systems providing interstory drift as state variable, but I remark that the general principles of design can and should be applied on all types of monitoring.

## Slide 81: SPECIMEN CONSTRUCTION

## Slide 82: SPECIMEN CONSTRUCTION

## Slide 83: Represented building
Building description:
2 stories commercial building
Column grid: 3x3 m
300x300 mm columns, 300x500 mm beams
Column
Beam
Slab

## Slide 84: SPECIMEN DETAILS

## Slide 85: LPMS

## Slide 86: INPUT DISPLACEMENT
Model of the 2dof system
m1 = 4685 kN
m2 = 3515 kN
ω1 = 1,5 Hz
ξ = 5%

## Slide 87: STRAIN MONITORING
Slab casting easily recognizable
Daily thermal variation in the order of 5-10 me, consistent with the daily thermal excursion inside the lab
Creep/shrinkage effects observed as a slow contraction of the bars

## Slide 89: testing ON SMALL-SCALE SPECIMENS
Calibration tests
Earthquake simulations on small scale metal frame
Strain on the carrier
Strain outside the carrier
Adhesion tests on strain sensor support layer
Cyclic tests on small scale rc specimens

## Slide 90: OBJECTIVES
Define a rational framework for SHM system design .
In the context of this framework:
  Study most relevant aspects of monitoring systems based on interstory drift monitoring;
  Evaluate by experimental testing a monitoring system for RC buildings;
  Develop a monitoring system for precast industrial buildings;
Introduce a method based on acceleration and tilt measurements and present a possible industrial deployment.

## Slide 91: ERRORS